## Slide 1: Machine Learning-based Occupancy Estimation for energy conservation in buildings
By Shivaji Ganesh.

## Slide 2: Introduction
In buildings, a large chunk of energy is spent on HVAC and lighting systems.
Recent studies have shown that occupant information (e.g., number, presence, behavior, activities) is a major input for control approaches in energy efficient buildings.
Studies have demonstrated energy can be saved upto 30% in buildings where the occupancy pattern was known.
Supervised machine learning models are used to gain inference about occupancy count from the deployed sensor nodes in the room.

## Slide 3: Research Objectives
There are some features which show a change when occupancy count changes like co2, temperature etc. So, we are using data of those features to coach the model. We are using data collected by co2, temperature, humidity sensors. and that we have classified the state of room into 4 types.
Data preprocessing techniques to switch the data into well organized manner.
The performance comparison in terms of estimation accuracy and F1 score is noted for various ML algorithms.

## Slide 4: Issues to be addressed
To accurately estimate the number of occupants in a room using non-intrusive sensors to design power efficient buildings.
Previous works are done to count people using cameras(privacy issues).
Overcoming user identification or privacy violation

## Slide 5
Hardware sensors & IoT Devices
Co2 level
humidity
Temp.
Sensors data
gateway
(node mcu)
Internet
Data aggregation
Wifi interface
visualisation
Processing & analytics
storage
Number of occupants
Real time occupancy estimation

## Slide 6: Methodology
Phase-1: Constructing sensor node
(sensors used – co2, temp, humidity
Micro-controller – Node MCU).
Phase-2: Collecting data from sensors and pushing into cloud.

## Slide 7: Phase-III : Data Pre-processing (Dataset Construction)
A few seconds of variation was present between the arrival times of packets of different nodes. We merged the time-stamps within a given time frame into a common vector.
Feature vectors with missing data were simply deleted.
The manually logged ground truth of occupancy count
was appended
levels:
  0 : Empty(0)
  1 - 2 : Low(1)
  3 - 4 : Fair(2)
  5 - 6 : High(3)

## Slide 8: Phase-IV : Machine Learning Algorithms
K-Nearest Neighbours
Support Vector Machine
Random Forest
Naive Bayes
DT
KNN
SVM
RF
NB
Supervised
Decision Trees

## Slide 9: Results
Algorithm | Accuracy | F1-score
KNN | 87.12 | 86.86
SVM | 80.7 | 80.2
Decision Trees | 84.55 | 84.4
Random Forest | 85.1 | 84.9
Naïve Bayes | 60 | 59
Different algorithms were applied on the data and metrics were noted.
KNN performed better among all.
Naïve Bayes is comparatively low.
KNN is tested for various k’s and finally k=22 gave highest accuracy.

## Slide 10: Practical Applications
This model can be used within indoor places automating HVAC systems.
When space is empty , doesn’t need to turn ON the Appliances. The energy can be conserved by deactivating them.
This solution can also be implemented by large buildings which wastes large amount of energy on HVAC systems.

## Slide 11: References
T. Vafeiadis et al., "Machine Learning Based Occupancy Detection via the Use of Smart Meters," 2017 International Symposium on Computer Science and Intelligent Controls (ISCSIC), Budapest, Hungary, 2017, pp. 6-12, doi: 10.1109/ISCSIC.2017.15.
A. P. Singh, V. Jain, S. Chaudhari, F. A. Kraemer, S. Werner and V. Garg, "Machine Learning-Based Occupancy Estimation Using Multivariate Sensor Nodes," 2018 IEEE Globecom Workshops (GC Wkshps), Abu Dhabi, United Arab Emirates, 2018, pp. 1-6, doi: 10.1109/GLOCOMW.2018.8644432.
Schwee, Jens Hjort; Johansen, Aslak; Jørgensen, Bo Nørregaard; Kjærgaard, Mikkel Baun; Mattera, Claudio Giovanni; Sangogboye, Fisayo Caleb; et al. (2019): Room-level occupant counts and environmental quality from heterogeneous sensing modalities in a smart building. Springer Nature. Dataset. https://doi.org/10.6084/m9.figshare.9959417.v1

## Slide 12
Thank You